## Slide 1
ARM

## Slide 2
ARM history
Acorn RISC Machine (Acorn Computers, UK)
  Design initiated 1983, first silicon 1985
  Licensing model allows for custom designs (contrast to x86)
    Does not produce their own chips
    Companies customize base CPU for their products
    PA Semiconductor (fabless, SoC startup acquired by Apple for its A4 design that powers iPhone/iPad)
    ARM estimated to make $0.11 on each chip (royalties + license)
  Runs 98% of all mobile phones (2005)
    Per-watt performance better than x86

## Slide 3
ARM architecture
RISC architecture
  32-bit reduced instruction set machine inspired by Berkeley RISC (Patterson, 1980-1984)
  Fewer instructions
    Complex instructions handled via multiple simpler ones
    Results in a smaller execution unit
  Only loads/stores to and from memory
  Uniform-size instructions
    Less decoding logic
    16-bit in Thumb mode to increase code density

## Slide 4
ARM architecture
ALU features
  Conditional execution built into many instructions
    Less branches
    Less power lost to stalled pipelines
    No need for branch prediction logic
  Operand bit-shifts supported in certain instructions
    Built-in barrel shifter in ALU
    Bit shifting plus ALU operation in one (similar to x86 lea)
  Support for 3 operand instructions
    <R> = <Op1> OP <Op2>

## Slide 5
ARM architecture
Control state features
  Shadow registers (pre v7)
    Allows efficient interrupt processing (no need to save registers onto stack)
    Akin to Intel hyperthreading
  Link register
    Stores return address for leaf functions (no stack operation needed)

## Slide 6
ARM architecture
Advanced features
  SIMD (NEON) to compete with x86 at high end
    mp3, AES, SHA support
  Hardware virtualization
    Hypervisor mode
  Jazelle DBX (Direct Bytecode eXecution)
    Native execution of Java
  Security
    No-execute page protection

## Slide 7
x86 vs ARM
Key architectural differences (x86 v. ARM)
  CISC vs. RISC
    ARM with less “legacy” instructions to implement
    Legacy instructions impact per-watt performance
    Atom (stripped-down 80386 core)
      Once a candidate for the iPad
  State pushed onto stack vs. swapped from shadow registers
  Bit shifting separate, explicit instructions vs. built-in shifts
  Memory locations usable as ALU operands vs. load/store only
  Mostly 2 operand instructions ( <D> = <D> OP <S> ) vs. 3-operand

## Slide 8
ARM vs. x86
Other differences
  Intel is the only producer of x86 chips and designs
    No SoC customization (everyone gets same hardware)
    Must wait for Intel to give you what you want
    ARM allows Apple to differentiate itself
  Intel and ARM
    XScale: Intel's version of ARM sold to Marvell in 2006
    Speculation
      Intel advantage on process to make RISC/CISC moot
      Leakage current will eventually dominate power consumption (versus switching current)
      Make process advantage bigger than custom design + RISC advantage (avoid wasting money on license)
      Not successful